## Slide 1
Chapter 3 – Part 2
MEDIA ACCESS CONTROL

## Slide 2
Data link layer divided into two functionality-oriented sublayers
Link Layer Control (LLC)
MAC
Responsible for error and flow control
Control
Responsible framing and MAC address and Multiple Access Control

## Slide 3: Multiple Access
Problem: When two or more nodes transmit at the same time, their frames will collide and the link bandwidth is wasted during collision
  How to coordinate the access of multiple sending/receiving nodes to the shared link???
Solution: We need a protocol to coordinate the transmission of the active nodes
These protocols are called Medium or Multiple Access Control (MAC) Protocols belong to a sublayer of the data link layer called MAC (Medium Access Control)
What is expected from Multiple Access Protocols:
  Main task is to minimize collisions in order to utilize the bandwidth by:
    Determining when a station can use the link (medium)
    what a station should do when the link is busy
    what the station should do when it is involved in collision

## Slide 4
Taxonomy of multiple-access protocols

## Slide 5
RANDOM ACCESS/ Contention protocol
In random access or contention methods, no station is superior to another station and none is assigned the control over another.
No station permits, or does not permit, another station to send.
At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.
Two terms can be explained as follows.
Random access: because there is no schedule time defined for a station to transmit. Transmission is random among the stations.
Contention: because stations compete with each other to access the channel.

## Slide 6
ALOHA Carrier Sense Multiple Access
Carrier Sense Multiple Access with Collision Detection
Carrier Sense Multiple Access with Collision Avoidance
Four Random access protocols

## Slide 7: ALOHA – meaning
Was developed at the university of Hawaii in early 1970
Derived from a compound word of the Hawaiian words
ALO means “share”
Ha means “ essence of life”

## Slide 8: Pure ALOHA
This is a simple and elegant protocol
Each station sends a frame whenever it has a frame to send.
However , the channel is shared among all the stations, there are chances of collision between frames from different stations.
After sending frame, the station simply wait for an ack.
If the acknowledgement does not arrive after a time-out-period expires, the station retransmits the frame.
A collision involves two or more stations. If all of them again retransmit then there will be collision again.

## Slide 9: Pure ALOHA (1)
Improvement 1:
After a time-out period, wait for a random amount of time and then try again.
This randomness will help avoid more collisions.
This random time is called back-off Time. Tb
Improvement 2:
After a number of retransmissions attempts Kmax, a station must give up and try later.
Usually Kmax = 15

## Slide 10: Pure ALOHA (2)
How much should be the time out period?
The time out period = maximum possible RTT
RTTmax is the twice the amount of time taken to send a frame between two farthest stations on a link.
RTT = 2 * Tp , where Tp-Propagation Delay

## Slide 11: Pure ALOHA(3)
The back-off Time (Tb)
The back off time Tb is a random value that normally depends on k (no. of retransmissions).
Usually the Tb increases as number of attempts increases.

## Slide 12
Pure ALOHA Protocol Description (4)
  All frames from any station are of fixed length (L bits)
  Stations transmit at equal transmission time (all stations produce frames with equal frame lengths).
  A station that has data can transmit at any time
  After transmitting a frame, the sender waits for an acknowledgment for an amount of time (time out) equal to the maximum round-trip propagation delay = 2* tp
  If no ACK was received, sender assumes that the frame or ACK has been destroyed and resends that frame after it waits for a random amount of time
  If station fails to receive an ACK after repeated transmissions, it gives up

## Slide 13
Frames in a pure ALOHA network

## Slide 14
Procedure for ALOHA protocol

## Slide 15: Pure ALOHA (7)
Vulnerable Time: The length of time in which there is a probability of collision.
For ALOHA
Where Tf is the average time required to transmit one frame.
Vulnerable Time = 2 * Tf

## Slide 16
Vulnerable time for pure ALOHA protocol
If the frame transmission time is Tf sec, then the vulnerable time is = 2 * Tf sec.
This means no station should send during the T-sec before this station starts transmission and no station should start sending during the T-sec period that the current station is sending.

## Slide 17
  Channel utilization or efficiency or Throughput is the percentage of the transmitted frames that arrive successfully (without collisions) or the percentage of the channel bandwidth that will be used for transmitting frames without collisions
  ALOHA Maximum channel utilization is 18% (i.e, if the system produces F frames/s, then 0.18 * F frames will arrive successfully on average without the need of retransmission).
Pure ALOHA - Efficiency

## Slide 18
The throughput for pure ALOHA is S = G × e −2G .
The maximum throughput
Smax = 0.184 when G= (1/2).

## Slide 19: Random Access – Slotted ALOHA
Time is divided into slots equal to a frame transmission time (Tf)
A station can transmit at the beginning of a slot only
If a station misses the beginning of a slot, it has to wait until the beginning of the next time slot.
A central clock or station informs all stations about the start of a each slot
Maximum channel utilization is 0.368% (Approx. 37%)

## Slide 20
Frames in a slotted ALOHA network

## Slide 21
Vulnerable time for slotted ALOHA protocol

## Slide 22
The throughput for slotted ALOHA is S = G × e−G .
The maximum throughput Smax = 0.368 when G = 1.

## Slide 23
Efficiency of ALOHA
S = throughput =(success rate)
G = offered load rate= new frames+ retransmitted
= Total frames presented to the link per
the transmission time of a single frame
0.5
1.0
1.5
2.0
0.1
0.2
0.3
0.4
Pure Aloha
Slotted Aloha

## Slide 24
Advantage of ALOHA protocols
  A node that has frames to be transmitted can transmit continuously at the full rate of channel (R bps) if it is the only node with frames
  Simple to be implemented
  No master station is needed to control the medium
Disadvantage
  If (M) nodes want to transmit, many collisions can occur and the rate allocated for each node will not be on average R/M bps
  This causes low channel utilization

## Slide 25: Random Access – Carrier Sense Multiple Access (CSMA)
  Each station senses the channel before sending a frame.
  If the channel is busy, devices wait before transmitting.
This can reduce the possibility of collision but it cannot eliminate it.
  Collision can only happen when more than one station begin transmitting within the propagation time period..

## Slide 26: CSMA

## Slide 27
Random Access – Carrier Sense Multiple Access (CSMA)
Vulnerable time for CSMA is the maximum propagation time
The longer the propagation delay, the worse the performance of the protocol because of the above case.

## Slide 28: Types of CSMA Protocols
  Different CSMA protocols that determine:
  What a station should do when the medium is idle?
  What a station should do when the medium is busy?
    Non-Persistent CSMA
    1-Persistent CSMA
    p-Persistent CSMA

## Slide 29
1- Persistent
After a station finds the line idle, it sends the frame immediately (i,.e with probability 1).
This method has a highest chance of collisions.
Non-persistent
A station that has a frame to send senses the channel. If the line is idle , it sends immediately else it waits a random amount of time and then senses the channel again.
This approach reduces the chances of collision , because it is unlikely that two station chooses the same random time and sense the channel simultaneously.
P-Persistent
It is used if the channel is divided into time slot equal to maximum Tp or more than Tp.
It combines the advantages of above two methods.
In this method, after the station finds the channel idle it transmits with a probability p.
With probability q=1-p it differs until the next slot. If that slot is also idle, it either transmits or differs again, with probability p and q. This process is repeated until the station sends the frame or other station has begun transmission.

## Slide 30
Behavior of three persistence methods

## Slide 31
Flow diagram for three persistence methods

## Slide 32
CSMA/CD (Collision Detection)
CSMA (all previous methods) has an inefficiency:
  If a collision has occurred, the channel is unstable until colliding packets have been fully transmitted
CSMA/CD (Carrier Sense Multiple Access with Collision Detection) overcomes this as follows:
  While transmitting, the sender is listening to medium for collisions.
  Sender stops transmission if collision has occurred reducing channel wastage .
CSMA/CD is Widely used for bus topology LANs (IEEE 802.3, Ethernet).

## Slide 33
of its own
signal, it means collision occurred

## Slide 34
Collision of the first bit in CSMA/CD

## Slide 35: CSMA/CD Protocol
Use one of the CSMA persistence algorithm
(non-persistent, 1-persistent, p-persistent) for transmission
If a collision is detected by a station during its transmission then it should do the following:
  Abort transmission and
  Transmit a jam signal (48 bit) to notify other stations of collision
  After sending the jam signal, backoff (wait) for a random amount of time, then Transmit the frame again

## Slide 36: CSMA/CD
Question: How long does it take to detect a collision?
Answer: In the worst case, twice the maximum propagation delay of the medium
Note: a = maximum propagation delay

## Slide 37: CSMA/CD
Restrictions of CSMA / CD:
  Packet transmission time should be at least as long as the time needed to detect a collision (2 * maximum propagation delay + jam sequence transmission time)
  Otherwise, CSMA/CD does not have an advantage over CSMA

## Slide 38: Exponential Backoff Algorithm
Ethernet uses the exponential backoff algorithms to determine the best duration of the random waiting period after the collision happens
Algorithm:
  Set “slot time” equal to 2*maximum propagation delay + Jam sequence transmission time (= 51.2 usec for Ethernet 10-Mbps LAN)
  After Kth collision, select a random number (R) between 0 and
  2k –1 and wait for a period equal to (R*slot time) then retransmit when the medium is idle, for example:
    After first collision (K=1), select a number (R) between 0 and 21 –1 {0 ,1} and wait for a period equal to R*slot times (Wait for a period 0 usec or 1x51.2 usec) then retransmit when the medium is idle
  Do not increase random number range, if K=10
     Maximum interval {0 – 1023}
  Give up after 16 unsuccessful attempts and report failure to higher layers

## Slide 39
Flow diagram for the CSMA/CD
N=N+1
N=0
N==16
Abort
N < 10
K=N
K=10
Choose R between 0 & 2k - 1
Wait R*slot time
No
No
Yes
Yes

## Slide 40: Exponential Backoff Algorithm……
Reduces the chance of two waiting stations picking the same random waiting time
When network traffic is light, it results in minimum waiting time before transmission
As congestion increases ( traffic is high), collisions increase, stations backoff by larger amounts to reduce the probability of collision.
Exponential Back off algorithm gives last-in, first-out effect
  Stations with no or few collisions will have the chance to transmit before stations that have waited longer because of their previous unsuccessful transmission attempts.

## Slide 41: Performance of Random Access Protocols
Simple and easy to implement
Decentralized (no central device that can fail and bring down the entire system)
In low-traffic, packet transfer has low-delay
However, limited throughput and in heavier traffic, packet delay has no limit.
In some cases, a station may never have a chance to transfer its packet. (unfair protocol)
A node that has frames to be transmitted can transmit continuously at the full rate of channel (R) if it is the only node with frames
If (M) nodes want to transmit, many collisions can occur and the rate for each node will not be on average R/M

## Slide 42: Ethernet – 802.3
History
  Developed by Bob Metcalfe and others at Xerox PARC in mid-1970s
  Standardized by Xerox, DEC, and Intel in 1978
  LAN standards define MAC and physical layer connectivity
    IEEE 802.3 (CSMA/CD - Ethernet) standard – originally 2Mbps
    IEEE 802.3u standard for 100Mbps Ethernet
    IEEE 802.3z standard for 1,000Mbps Ethernet
CSMA/CD: Ethernet’s Media Access Control (MAC) policy
  CS = carrier sense
    Send only if medium is idle
  MA = multiple access
  CD = collision detection
    Stop sending immediately if collision is detected

## Slide 43: Ethernet Addresses
End nodes are identified by their Ethernet Addresses (MAC Address or Hardware Address) which is a unique 6 Byte address.
MAC Address is represented in HexaDecimal format e.g 00:05:5D:FE:10:0A
The first 3 bytes identify a vendor (also called prefix) and the last 3 bytes are unique for every host or device

## Slide 44: Ethernet
Name | Cable | Topology | Nodes/seg | Max segment length | speed
10Base5 (Thicknet) | Thick coax | Bus | 100 | 500 m with at most 4 repeaters | 10mbps
10Base2 (Thinnet) | Thin Coax | Bus | 30 | 185 m with at most 4 repeaters | 10mbps
10Base-T | Twisted pair UTP cat3/cat5 | Star | 1024 | 100 m with at most 4 hubs | 10mbps
10 Base-F | Multimode/sibglemode Fiber optic cable | Tree | 1024 | 2000m | 10mbps

## Slide 45: Ethernet
The number 10: At the front of each identifier, 10 denotes the standard data transfer speed over these media - ten megabits per second (10Mbps).
The word Base: Short for Baseband, this part of the identifier signifies a type of network that uses only one carrier frequency for signaling and requires all network stations to share its use.
The segment type or segment length: This part of the identifier can be a digit or a letter:
· Digit - shorthand for how long (in meters) a cable segment may be before attenuation sets in. For example, a 10Base5 segment can be no more than 500 meters long.
Letter - identifies a specific physical type of cable.

## Slide 46: 10Base5 Cabling
Uses Vampire Taps.
A pin is very carefully forced halfway into coaxial cable’s core.
Difficult to install.

## Slide 47: 10Base2 Cabling
Uses BNC connectors.
Easier to use
More reliable
Thinnets are Easy to install
But can run only 185 meter/segment

## Slide 48: 10Base 2 and 10 base5
Disadvantages
Detecting cable breaks is difficult
Excessive length
Bad taps or loose connectors can be a problem.
Installation is difficult

## Slide 49: 10BaseT cabling
UTP connectors (RJ -45 connectors)
Easy to install
Easy to maintain
Fault detection and
Fault isolation is easy
Hub with RJ-45 connectors

## Slide 50: Cabling

## Slide 51: 10BaseF cabling
A fiber optic connector terminates the end of a fiber optic cable, and enables quicker connection and disconnection than splicing.
It has to be aligned properly to the microscopic glass fibers completely in order to allocate for communication.
In all, there are nearly 100 fiber optic connectors in the market, but only a few represents the majority of the market —
LC connector, SC connector, ST connector, FC connector etc.
Expensive due to the cost of connectors and terminators.
But excellent noise immunity

## Slide 52: Fiber optic Connectors
SC - Subscriber Connector
LC - Lucent Connector
FC - Ferrule Connector
ST - Straight Tip

## Slide 53: Fiber optic Connectors

## Slide 54: IEEE 802.3 (Ethernet) Frame format

## Slide 55: IEEE 802.3 (Ethernet) Frame format
PREAMBLE – Ethernet frame starts with 7-Bytes Preamble. This is pattern of alternative 0’s and 1’s which indicates starting of the frame and allow sender and receiver to establish bit synchronization.
Start of frame delimiter (SFD) – This is a 1-Byte field which is always set to 10101011. SFD indicates that upcoming bits are starting of frame, which is destination address.

## Slide 56
Destination Address – This is 6-Byte field which contains the MAC address of machine for which data is destined.
Source Address – This is a 6-Byte field which contains the MAC address of source machine.

## Slide 57
Length – Length is a 2-Byte field, which indicates the length of entire Ethernet frame. This 16-bit field can hold the length value between 0 to 65534, but length can not be larger than 1500 because of some own limitations of Ethernet.
Data – This is the place where actual data is inserted, also known as Payload. Both IP header and data will be inserted here, if Internet Protocol is used over Ethernet. The maximum data present may be as long as 1500 Bytes. In case data length is less than minimum length i.e. 46 bytes, then padding 0’s is added to meet the minimum possible length.
Cyclic Redundancy Check (CRC) – CRC is 4 Byte field. This field contains 32-bits hash code of data, which is generated over Destination Address, Source Address, Length and Data field. If the checksum computed by destination is not same as sent checksum value, data received is corrupted.

## Slide 58: Fast Ethernet
100 Mbps bandwidth
Uses same CSMA/CD media access protocol and packet format as in Ethernet.
100BaseTX (UTP) and 100BaseFX (Fiber) standards
Physical media :-
    100 BaseTX - UTP Cat 5e
    100 BaseFX - Multimode / Singlemode Fiber
Full Duplex/Half Duplex operations.

## Slide 59: Fast Ethernet
Maximum Segment Length
    100 Base TX - 100 m
    100 Base FX - 2 Km (Multimode Fiber)
    100 Base FX - 20 km (Singlemode Fiber)

## Slide 60: Gigabit Ethernet
1 Gbps bandwidth.
Uses same CSMA/CD media access protocol as in Ethernet and is backward compatible (10/100/100 modules are available).
1000BaseT (UTP), 1000BaseSX (Multimode Fiber) and 1000BaseLX (Multimode/Singlemode Fiber) standards.
Maximum Segment Length
    1000 Base T - 100m (Cat 5e/6)
    1000 Base SX - 275 m (Multimode Fiber)
    1000 Base LX - 512 m (Multimode Fiber)
    1000 Base LX - 20 Km (Singlemode Fiber)
    1000 Base LH - 80 Km (Singlemode Fiber)

## Slide 61: 10 Gig Ethernet
10 Gbps bandwidth.
Uses same CSMA/CD media access protocol as in Ethernet.
Propositioned for Metro-Ethernet
Maximum Segment Length
    1000 Base-T - Not available
    10GBase-LR - 10 Km (Singlemode Fiber)
    10GBase-ER - 40 Km (Singlemode Fiber)

## Slide 62
End of MAC

## Slide 63
Lets take a Quiz
1. The data link layer takes the packets from _________ and encapsulates them into frames for transmission. a) network layer b) physical layer c) transport layer d) application layer
2. Which one of the following task is not done by data link layer? a) framing b) error control c) flow control d) channel coding

## Slide 64
3. Which sublayer of the data link layer performs data link functions that depend upon the type of medium? a) logical link control sublayer b) media access control sublayer c) network interface control sublayer d) none of the mentioned
4. Header of a frame generally contains a) synchronization bytes b) addresses c) frame identifier d) all of the mentioned

## Slide 65
5. Automatic repeat request error management mechanism is provided by a) logical link control sublayer b) media access control sublayer c) network interface control sublayer d) none of the mentioned
6. Which one of the following is a data link protocol? a) ethernet b) point to point protocol c) hdlc d) all of the mentioned
7. The technique of temporarily delaying outgoing acknowledgements so that they can be hooked onto the next outgoing data frame is called a) piggybacking b) cyclic redundancy check c) fletcher’s checksum d) none of the mentioned

## Slide 66
8. When does the station B send a positive acknowledgement (ACK) to station A in Stop and Wait protocol? a. only when no error occurs at the transmission level b. when retransmission of old packet in a novel frame is necessary c. only when station B receives frame with errors d. all of the above
9.Which provision can resolve / overcome the shortcomings associated with duplication or failure condition of Stop and Wait Automatic Repeat Request protocol especially due to loss of data frames or non-reception of acknowledgement? a. Provision of sequence number in the header of message b. Provision of checksum computation c. Both a & b d. None of the above

## Slide 67
What are the frames issued by the secondary station of HDLC ,known as? a. Link b. Command c. Response d. None of the above